## Slide 1
MAJOR PROJECT PRESENTATION
AI-Based Smart Eco
Air Pollution Control System
An IoT + AI + ML Integrated Source-Level Purification System
Using Eco-Friendly Bamboo & Charcoal Filtration
Team DeepThink | Projexa ID: 26E3261 Shubham (2301730100) • Suryansh (2301730126) Brijesh (2301730134) • Kartik Yadav (2301730099) Supervisor: Mr. Anurag Singh | CSE-AI&ML (Sec-B) | May 2026
🌿
K.R. MANGALAM
UNIVERSITY
Dept. of CSE
SoET
B.Tech CSE
AI & ML — 2023–27
Presented for: Final Major Project Evaluation | GitHub: shubham055555/AI-Based-Smart-Eco-Air-Pollution-Control-System

## Slide 2
Presentation Agenda
01
Problem Statement & Motivation
02
Literature Review & Gap Analysis
03
Objectives
04
System Architecture & Design
05
Technology Stack & Tools
06
Hardware Build & Methodology
07
ML Model Design & Training
08
Experimental Results
09
Comparative Advantages & Cost
10
Conclusion & Future Work
DeepThink — K.R. Mangalam University | Major Project 2025–26

## Slide 3
Problem Statement
Air pollution kills ~7 million people annually (WHO, 2022). Yet most solutions are reactive, expensive, and unsustainable.
⚠️ Reactive Systems
Act AFTER pollutants spread — too late for source-level control
💸 High Cost
HEPA-based purifiers cost ₹8,000–₹25,000; inaccessible for small industries
🗑️ Non-Biodegradable
Synthetic HEPA filters create secondary environmental waste
🔧 No Automation
Manual activation — no real-time adaptive intelligence
📊 No Prediction
No ML-based forecasting; systems only react to current readings
📍 No Source Control
No solution targets localized point sources like chimneys, workshops
DeepThink — K.R. Mangalam University | Major Project 2025–26

## Slide 4
Motivation
Delhi & Gurugram PM2.5 frequently exceeds 300 µg/m³ — 12× the WHO safe limit of 25 µg/m³
7M
Premature deaths/year due to PM2.5 + toxic gases (WHO 2022)
300+
µg/m³ PM2.5 in cities like Delhi — 12× WHO limit
₹25K
Cost of conventional HEPA purifiers — inaccessible for most
0
Existing systems with unified IoT + ML + eco-filtration (gap in literature)
This project is motivated by the urgent need for a low-cost, eco-friendly, AI-driven system that controls
pollution at its source — before it spreads — using sustainable bamboo & charcoal filtration.
DeepThink — K.R. Mangalam University | Major Project 2025–26

## Slide 5
Literature Review & Gap Analysis
Study / Author | Contribution | Limitation
Saha et al. (2017) — IoT Monitoring | Real-time IoT-based AQ sensing framework | No active remediation
Ayele & Mehta (2018) — ML Prediction | ML-based pollution trend prediction | No hardware filtration
Munera et al. — Smart City Review | 47 IoT deployments analyzed | No unified predict+control system
Bharath Kumar Sai et al. | 87–92% accuracy with MQ135+ML | No eco-filtration, no source control
Li et al. (2019) — Bamboo Carbon | Bamboo activated carbon — effective adsorption | Not integrated with IoT/AI
🎯 Research Gap Addressed: No prior work combines real-time IoT monitoring + ML prediction + eco-friendly filtration
in a single deployable prototype. This project directly bridges this gap.
DeepThink — K.R. Mangalam University | Major Project 2025–26

## Slide 6
Project Objectives
01
Design & implement source-level IoT air pollution control using eco-friendly filtration
02
Collect real sensor data (PM2.5, MQ135, DHT11) and train ML models for AQI classification
03
Evaluate filtration efficiency through 10 controlled experimental trials
04
Achieve system actuation response time < 3 seconds from threshold exceedance
05
Validate Logistic Regression and Decision Tree models; compare classification accuracy
06
Develop an affordable solution (target: < ₹2,000) for schools, workshops & small industries
07
Minimize environmental impact by replacing synthetic HEPA with bamboo & charcoal filters
08
Enable both indoor and outdoor deployment in pollution-intensive environments
DeepThink — K.R. Mangalam University | Major Project 2025–26

## Slide 7
System Architecture
DeepThink — K.R. Mangalam University | Major Project 2025–26

## Slide 8
System Architecture — Description
Layer 1 — Air Quality Sensors
DHT11 (Temp & Humidity), PM2.5 (GP2Y1010AU0F, 0–500 µg/m³), MQ135 Gas Sensor (10–1000 ppm). Sensors sample at 1-second intervals via Arduino's 10-bit ADC.
Layer 2 — Data Processing & Control (Arduino UNO)
Embedded C firmware processes raw ADC values into calibrated readings. Compares against CPCB thresholds: PM2.5 > 100 µg/m³ or MQ135 > 200 ppm triggers actuation.
Layer 3 — Decision & Actuation
Rule-based AI: Low power mode below threshold. Fan at base speed when threshold exceeded. Fan at full speed when PM2.5 > 200 µg/m³ (critical level). ±10 µg/m³ hysteresis prevents motor cycling.
Layer 4 — Eco-Friendly Filtration
Polluted air passes through: (1) Pre-filter mesh — coarse PM. (2) Bamboo fiber layer — fine particulate. (3) Activated charcoal — gases, VOCs, odors. 73.8% PM2.5 reduction achieved.
Layer 5 — Output & Monitoring
Clean air released. I2C LCD shows real-time PM2.5, MQ135, AQI class. Serial output to ML inference pipeline. Response time: 2.4 seconds average.
DeepThink — K.R. Mangalam University | Major Project 2025–26

## Slide 9
Technology Stack / Data & Resources
Hardware
Arduino UNO · PM2.5 Sensor (GP2Y1010AU0F)
MQ135 · DHT11 · DC Motor+Fan · I2C LCD
Embedded SW
Embedded C / Arduino IDE
Hysteresis control · Serial data output
AI / ML
Logistic Regression (91.3%) · Decision Tree (88.7%)
Python 3.10 · scikit-learn 1.3 · SMOTE
Filtration
Bamboo fiber pre-filter
Activated charcoal adsorption layer
Monitoring
I2C LCD real-time AQI display
Serial logging → CSV for ML pipeline
DeepThink — K.R. Mangalam University | Major Project 2025–26

## Slide 10
Hardware Design & Physical Build
Build Specifications
Enclosure:
Acrylic — 30cm × 20cm × 15cm
Airflow:
DC Motor (5V, 200mA) draws air inward
Filter Stack:
Pre-mesh → Bamboo Fiber → Charcoal
Sensor Zone:
Inlet: PM2.5 + MQ135 + DHT11
Display:
I2C LCD (16×2) shows AQI + PM2.5
Controller:
Arduino UNO (ATmega328P, 16MHz)
Power:
5V DC regulated supply
Cost:
~₹1,520 total (~USD 18)
DeepThink — K.R. Mangalam University | Major Project 2025–26

## Slide 11
Methodology — System Workflow
1
Data Collection
PM2.5, MQ135,
DHT11 @ 1s intervals
2
Data Processing
Arduino ADC →
Calibrated values
3
AI Decision
Threshold logic
+ adaptive fan speed
4
Filtration
Bamboo → Charcoal
multi-layer purification
5
ML Prediction
LR + DT models
AQI class forecast
// Key AI Decision Logic (Embedded C — Arduino)
if (pm25 > PM25_HIGH) analogWrite(FAN_PIN, 255); // FULL speed
else if (pm25 > PM25_THRESHOLD || (mq135 > MQ135_THRESHOLD && humidity < HUMIDITY_GATE))
analogWrite(FAN_PIN, 180); // BASE speed
else analogWrite(FAN_PIN, 0); // STANDBY
DeepThink — K.R. Mangalam University | Major Project 2025–26

## Slide 12
Machine Learning — Model Design & Training
Dataset & Features
10 controlled trials × ~1,800 records = 18,000 total
3 environments: Lab (incense), Workshop, Classroom
Feature Vector (5 features):
• PM2.5 concentration (µg/m³)
• MQ135 output (ppm)
• Temperature (°C)
• Relative Humidity (%)
• Time-of-day encoding
Target: 4-class AQI label (CPCB standards)
Good ≤50 | Moderate 51–100 | Unhealthy 101–200 | Hazardous >200
Logistic Regression (Primary)
One-vs-Rest | Z-score normalization | C tuned via 5-fold CV
Train: 93.1% • Test: 91.3% • Macro F1: 90.9%
Hazardous class accuracy: 95.1%
Decision Tree (Secondary — Interpretable)
CART algorithm | Gini impurity | Max depth: 6 (pruned)
Train: 94.5% • Test: 88.7% • Macro F1: 87.8%
Top feature: PM2.5 (importance: 0.61), MQ135 (0.27)
Highly interpretable — suitable for embedded edge deployment
80:20 Train/Test split • SMOTE for class imbalance • scikit-learn 1.3
DeepThink — K.R. Mangalam University | Major Project 2025–26

## Slide 13
Results — Filtration Performance (10 Trials)
73.8%
PM2.5 Reduction
(340→89 µg/m³)
71.9%
MQ135 Reduction
(420→118 ppm)
2.4s
Mean Response Time
(vs 30–60s HEPA)
0/10
False Activations
(after humidity gating)
Chart: PM2.5 Inlet vs Outlet (µg/m³)
| Trial 1 | Trial 2 | Trial 3 | Trial 4 | Trial 5 | Trial 6 | Trial 7 | Trial 8 | Trial 9 | Trial 10
Inlet PM2.5 | 330 | 345 | 355 | 320 | 350 | 340 | 338 | 342 | 335 | 348
Outlet PM2.5 | 87 | 91 | 95 | 82 | 93 | 89 | 86 | 90 | 88 | 92
Chart: MQ135 Inlet vs Outlet (ppm)
| Trial 1 | Trial 2 | Trial 3 | Trial 4 | Trial 5 | Trial 6 | Trial 7 | Trial 8 | Trial 9 | Trial 10
Inlet MQ135 | 410 | 430 | 425 | 405 | 420 | 418 | 428 | 415 | 422 | 435
Outlet MQ135 | 116 | 120 | 122 | 112 | 119 | 118 | 121 | 115 | 117 | 123
DeepThink — K.R. Mangalam University | Major Project 2025–26

## Slide 14
Results — ML Model Performance
Chart: Model Comparison — Accuracy Metrics (%)
| Test Accuracy | Precision | Recall | F1-Score | Hazardous Class
Logistic Regression | 91.3 | 90.8 | 91.1 | 90.9 | 95.1
Decision Tree | 88.7 | 87.4 | 88.2 | 87.8 | 93.4
Chart: Decision Tree Feature Importance
| PM2.5 | MQ135 | Temperature | Humidity
Feature Importance | 61 | 27 | 8 | 4
Key Insights
• LR recommended as primary model
• DT best for edge/embedded (interpretable)
• PM2.5 + MQ135 = 88% predictive power
DeepThink — K.R. Mangalam University | Major Project 2025–26

## Slide 15
Comparative Advantages & Cost Analysis
Feature | Proposed System | Conventional HEPA
Filtration Media | Bamboo + Charcoal (biodegradable ✅) | Synthetic HEPA (non-biodegradable ❌)
ML Prediction | Yes — LR (91.3%) + DT (88.7%) ✅ | No ❌
Real-time AQI Classification | Yes (91.3% accuracy) ✅ | No ❌
Response Time | 2.4 seconds ✅ | 30–60 seconds ❌
Estimated Cost | ₹1,520 (~USD 18) ✅ | ₹8,000–₹25,000 ❌
Outdoor Deployment | Yes ✅ | Limited / No ❌
Source-Level Control | Yes ✅ | No — ambient only ❌
Chart: 
| This System | Entry HEPA Purifier | Mid-range HEPA | Premium HEPA
Cost (INR) | 1520 | 8000 | 15000 | 25000
DeepThink — K.R. Mangalam University | Major Project 2025–26

## Slide 16
Limitations & Future Research Directions
Current Limitations
Efficiency drops when PM2.5 > 500 µg/m³ (filter saturation in 2–3 hours)
Bamboo-charcoal filter needs replacement every 30–45 days
ML trained on 18,000 records from 10 trials — needs broader real-world validation
MQ135 cross-sensitivity to humidity >80% RH (mitigated but not eliminated)
ML inference currently on companion PC — not yet fully embedded on MCU
Future Research Directions
🤖
Embedded ML on ESP32 via TensorFlow Lite / Edge Impulse
☁️
ThingSpeak / AWS IoT Core cloud dashboard & alerts
🧠
LSTM deep learning for multi-step-ahead forecasting
🌍
Multi-month field deployment for diverse training data
☀️
Solar-powered (5W PV panel) for off-grid outdoor use
🗺️
Multi-node sensor network for spatial AQI mapping
DeepThink — K.R. Mangalam University | Major Project 2025–26

## Slide 17
Conclusion
✅
PM2.5 reduced by 73.8% (340 → 89 µg/m³) across 10 controlled trials
✅
MQ135 gaseous pollutants reduced by 71.9% (420 → 118 ppm)
✅
System response time: 2.4 seconds — 12× faster than HEPA purifiers
✅
Logistic Regression: 91.3% accuracy | Decision Tree: 88.7% accuracy
✅
Total hardware cost: ₹1,520 (~USD 18) — 5–16× cheaper than HEPA alternatives
✅
First system to unify IoT monitoring + ML prediction + eco-friendly filtration
"Smarter air. Greener planet. Healthier future." — Team DeepThink | K.R. Mangalam University | May 2026

## Slide 18
Thank You!
We welcome your questions and feedback.
S
Shubham
2301730100
S
Suryansh
2301730126
B
Brijesh
2301730134
K
Kartik Yadav
2301730099
Supervisor: Mr. Anurag Singh (Asst. Professor, CSE) | K.R. Mangalam University, Gurugram
B.Tech CSE AI & ML (Sec-B) | Project: AI-Based Smart Eco Air Pollution Control System | May 2026
GitHub: github.com/shubham055555/AI-Based-Smart-Eco-Air-Pollution-Control-System | Projexa Team ID: 26E3261
🏆 Shubham Sharma — Certified: 1M1B Green Internship (AICTE + Salesforce, Sep–Oct 2025) | Tableau + Sustainability + Live Project